IP Camera CGI User Manual

H.264  IP  Camera

TABLE OF CONTENTS

Version Release Notes	4

IP Camera CGI Summary	5

1 Audio/Video	6

param.cgi?cmd=getvideoattr	6

param.cgi?cmd=setvideoattr	7

param.cgi?cmd=getvencattr	8

param.cgi?cmd=setvencattr	9

param.cgi?cmd=getimageattr	10

param.cgi?cmd=setimageattr	10

param.cgi?cmd=getoverlayattr	11

param.cgi?cmd=setoverlayattr	12

param.cgi?cmd=getmobilesnapattr	12

param.cgi?cmd=setmobilesnapattr	12

param.cgi?cmd=getaencattr	13

param.cgi?cmd=setaencattr	13

param.cgi?cmd=getaudioinvolume	14

param.cgi?cmd=setaudioinvolume	14

2 Infrared LED Control	14

param.cgi?cmd=getinfrared	14

param.cgi?cmd=setinfrared	15

3 Network	15

param.cgi?cmd=getnetattr	15

param.cgi?cmd=setnetattr	16

param.cgi?cmd=gethttpport	17

param.cgi?cmd=sethttpport	17

param.cgi?cmd=getrtspport	17

param.cgi?cmd=setrtspport	17

param.cgi?cmd=getinternetip	18

param.cgi?cmd=getupnpattr	18

param.cgi?cmd=setupnpattr	18

4 Wi-Fi setting	19

param.cgi?cmd=getwirelessattr	19

param.cgi?cmd=setwirelessattr	19

param.cgi?cmd=searchwireless	20

param.cgi?cmd=chkwirelessattr	21

5 DDNS	22

param.cgi?cmd=get3thddnsattr	22

param.cgi?cmd=set3thddnsattr	23

6 PTZ	23

ptzctrl.cgi	23

preset.cgi	24

param.cgi?cmd=getptzcomattr	25

param.cgi?cmd=setptzcomattr	25

ptzup.cgi	26

ptzdown.cgi	26

ptzleft.cgi	26

ptzright.cgi	27

ptzzoomin.cgi	27

ptzzoomout.cgi	27

7 Motion detection and I/O Alarm	28

param.cgi?cmd=getmdattr	28

param.cgi?cmd=setmdattr	29

param.cgi?cmd=getioattr	30

param.cgi?cmd=setioattr	30

param.cgi?cmd=getmdalarm	30

param.cgi?cmd=setmdalarm	31

param.cgi?cmd=getrelayattr	32

param.cgi?cmd=setrelayattr	32

param.cgi?cmd=getschedule	33

param.cgi?cmd=setschedule	34

param.cgi?cmd=getalarmserverattr	35

8 User Management	35

param.cgi?cmd=getuserattr	35

param.cgi?cmd=setuserattr	36

getsetupflag.cgi	36

getstreamflag.cgi	37

getptzflag.cgi	37

9 Time Snapshot	37

param.cgi?cmd=getsnaptimerattr	37

param.cgi?cmd=setsnaptimerattr	38

10 FTP	38

param.cgi?cmd=getftpattr	38

param.cgi?cmd=setftpattr	39

11 SMTP	40

param.cgi?cmd=getsmtpattr	40

param.cgi?cmd=setsmtpattr	40

12 SD Card manipulation	41

sdfrmt.cgi	41

sdstop.cgi	41

13 System parameter settings	42

param.cgi?cmd=getserverinfo	42

param.cgi?cmd=getdevtype	42

param.cgi?cmd=getstreamnum	43

param.cgi?cmd=getservertime	43

param.cgi?cmd=setservertime	43

param.cgi?cmd=getntpattr	44

param.cgi?cmd=setntpattr	44

sysreset.cgi	45

sysreboot.cgi	45

backup.cgi	45

restore.cgi	46

upgrade.cgi	46

14 LOG	47

logsync.cgi	47

cleanlog.cgi	47

15 Appendix	47

Appendix II  Time zone	48

# Version Release Notes

| Version | Author | Date | Modified |
| --- | --- | --- | --- |
| 1.0 | Himmy Ho | 2011-07-30 | The first version |
| 1.1 | Franck Zhao | 2011-09-08 | Revised |

# IP Camera CGI Summary

All the CGI APIs is based http protocol, IP camera could be manipulated by CGI command in client or other web application .

- CGI authorization: The CGI listed below is required for authorization when it be used , and different CGI is not the same authority needed. A total of three authorizations: visitor,operator and Administrator . Authority set by the user on the device . IP camera support two specific authorization : Basic authorization in http protocol、Additional parameters directly in the cgi user name and password .

- Cgi methods to access:  In this article cgi only support get and post method ,   upgrade.cgi and restore.cgi only support post method .

Get (Example)

<form name="form2" method="get" action="cgi-bin/hi3510/cleanlog.cgi">

<input name="cururl" type="hidden" >

<input name="name" type="hidden" value="access">

</form>

Post (Example):

<form name="form5" method="post" target="retframe" enctype="multipart/form-data" action="cgi-bin/hi3510/upgrade.cgi" onSubmit="return upgrade()">

<td colspan="3"><input type="file" name="setting_file" >

<input type="submit" value=" submit" >

</form>

- Value of CGI returned : CGI can be divided into two types according to the return value:

To get the device status and parameters , return the text of device status and parameter if CGI is executed successfully. The format of return text is the same as javascript variable definition .

For example:

var bps_1="2048";

var fps_1="25";

var gop_1="50";

var brmode_1="1";

var imagegrade_1="1";

var width_1="704";

var height_1="576";

Return error message if  failed,for example:[Error]Get video attribution error! errcode is 0xa10e6008” .

To setup or manipulate device: This type of CGI will be return the reuslut text, If CGI is executed successfully ,”HTTP/1.0 200 OK” will be returned；otherise , for example: ”[Error][Data-Length:91] unrecongnized or incomplete command line.” it tells us the CGI parameter error.

You could put the CGI string into Web Browser to test the CGI, such as:

http://192.168.1.88/cgi-bin/hi3510/param.cgi?cmd=getvencattr&-chn=11

http://192.168.1.6/cgi-bin/hi3510/param.cgi?cmd=setvencattr&-chn=11&-fps=15

http://192.168.1.6/cgi-bin/getwifi.cgi

# 1 Audio/Video

## param.cgi?cmd=getvideoattr

| Function | To get video properties, main-stream / sub-stream resolution and video format |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=getvideoattr] |
| parameters | none |
| Return Value | videomode | 18:1VGA_1QVGA or 1D1_1CIF 19: 1VGA_1QQVGA or 1D1_1QCIF 21: 1QVGA_1QVGA or 1CIF_1CIF 22: 1QVGA_1QQVGA or 1CIF_1QCIF 24: 1QQVGA_1QVGA or 1QCIF_1CIF 25: 1QQVGA_1QQVGA or 1QCIF_1QCIF 31: 1HD720P_1HDQ720P 32: 1HD720P_1HDQQ720P 33: 1HDQ720P_1HDQ720P 34: 1HDQ720P_1HDQQ720P 35: 1HDQQ720P_1HDQ720P 36: 1HDQQ720P_1HDQQ720P |
|  | vinorm | P: 50Hz(PAL) N: 60Hz(NTSC) |
| Note | Attention: 1VGA resolution is 640x480 1QVGA resolution is 320x240 1QQVGA resolution is 160x112 1D1 resolution is PAL: 704x576, NTSC: 704x480 1CIF resolution is PAL: 352x288, NTSC: 352x240 1QCIF resolution is PAL: 176x144, NTSC: 176x112 1QVGA resolution is 320x240 1QQVGA resolution is 160x112 1HD720P resolution is 1280x720 1HDQ720P resolution is 640x352 1HDQQ720P resolution is 320x176 Attention: It is main-stream resolution in front of “_” ,followed by sub-stream resolution 1HD720P_1HDQ720P: main-stream resolution is 720P , sub-stream resolution is Q720P |
| Example | /cgi-bin/hi3510/param.cgi?cmd=getvideoattr |

## param.cgi?cmd=setvideoattr

| Function | To set video properties, main-stream / sub-stream resolution and video format |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd= setvideoattr&- videomode =&-vinorm=] |
| parameters | videomode | 18:1VGA_1QVGA or 1D1_1CIF 19: 1VGA_1QQVGA or 1D1_1QCIF 21: 1QVGA_1QVGA or 1CIF_1CIF 22: 1QVGA_1QQVGA or 1CIF_1QCIF 24: 1QQVGA_1QVGA or 1QCIF_1CIF 25: 1QQVGA_1QQVGA or 1QCIF_1QCIF 31: 1HD720P_1HDQ720P 32: 1HD720P_1HDQQ720P 33: 1HDQ720P_1HDQ720P 34: 1HDQ720P_1HDQQ720P 35: 1HDQQ720P_1HDQ720P 36: 1HDQQ720P_1HDQQ720P |
|  | vinorm | P: 50Hz(PAL) N: 60Hz(NTSC) |
| Return Value | Success: contain Success Failure: contain Error |
| Note | Attention: Type of CCD D1device can identify PAL or NTSC automatically , vinorm setting invalid Attention: 1VGA resolution is 640x480 1QVGA resolution is 320x240 1QQVGA resolution is 160x112 1D1 resolution is PAL: 704x576, NTSC: 704x480 1CIF resolution is PAL: 352x288, NTSC: 352x240 1QCIF resolution is PAL: 176x144, NTSC: 176x112 1QVGA resolution is 320x240 1QQVGA resolution is 160x112 1HD720P resolution is 1280x720 1HDQ720P resolution is 640x352 1HDQQ720P resolution is 320x176 Attention: It is main-stream resolution in front of “_” ,followed by sub-stream resolution 1HD720P_1HDQ720P: main-stream resolution is 720P , sub-stream resolution is Q720P Attention: Return Value: Time-consuming operation |
| Example | /cgi-bin/hi3510/param.cgi?cmd=setvideoattr&-videomode=31&-vinorm=P |
|  | /cgi-bin/hi3510/param.cgi?cmd=setvideoattr&-videomode=33 |
|  | /cgi-bin/hi3510/param.cgi?cmd=setvideoattr&-vinorm=N |

## param.cgi?cmd=getvencattr

| Function | To get video codec parameters |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/getvencattr.cgi [?-chn=] |
| parameters | chn | Stream Number: 11: main-stream 12: sub-stream |
| Return Value | bps_1 or bps_2 | Bit rate |
|  | fps_1 or fps_2 | Frame rate |
|  | gop_1 or gop_2 | Main frame interval |
|  | brmode_1 or brmode_2 | Video coding control: 0: Fixed rate 1: Variable bit rate |
|  | imagegrade_1 or imagegrade_2 | video encoding quality |
|  | width_1 or width_2 | Video width |
|  | height_1 or height_2 | Video height |
| Note | Attention: Suffix”_1” is main-stream parameters , Suffix “_2” is sub-stream parameters . |
| Example | /cgi-bin/hi3510/getvencattr.cgi?-chn=11 |

## param.cgi?cmd=setvencattr

| Function | To config video codec parameters |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=setvencattr&-chn=&-bps=&-fps=&-brmode=&-imagegrade=&-gop=] |
| parameters | chn | Channel number : 11: main-stream 12: sub-stream |
|  | bps | Bit Rate: 720P: range [1024 ~ 6144 kbps] D1: range [32 ~ 2048 kbps] CIF: range [32 ~ 512 kbps] QCIF: range [32 ~ 256 kbps] QVGA: range [32 ~ 512 kbps] VGA: range [32 ~ 2048 kbps] QQVGA: range [32 ~ 256 kbps] |
|  | fps | Frame rate: PAL: range [1 ~ 25] NTSC: range [1 ~ 30] |
|  | brmode | Video coding control: 0: Fixed rate 1: Variable bit rate |
|  | imagegrade | video encoding quality: range [1 ~ 6] AttentionThe smaller the value, the better the image quality, the larger the stream control |
|  | gop | Main frame interval: range [2 ~ 150] |
| Return Value | Success: contain Success Failure: contain Error |
| Note | None |
| Example | /cgi-bin/hi3510/param.cgi?cmd=setvencattr&-chn=11&-bps=1536&-fps=25&-brmode=1&-imagegrade=1&-gop=50 |
|  | /cgi-bin/hi3510/param.cgi?cmd=setvencattr&-chn=12&-bps=1536&-fps=25&-brmode=1&-imagegrade=1&-gop=50 |
|  | /cgi-bin/hi3510/param.cgi?cmd=setvencattr&-chn=11&-bps=1536&-fps=25 |

## param.cgi?cmd=getimageattr

| Function | To get image parameters |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=getimageattr] |
| parameters | None |
| Return Value | brightness | Brightness |
|  | saturation | Saturation |
|  | contrast | Contrast |
|  | hue | Color |
|  | scene | White Balance: auto indoor outdoor |
|  | flip | Image flip: on off |
|  | mirror | Image mirror: on off |
| Note | Different device type has different image parameters, reference toAppendix I: Definition of device type |
| Example | /cgi-bin/hi3510/param.cgi?cmd=getimageattr |

## param.cgi?cmd=setimageattr

| Function | To set image parameters |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=setimageattr&-brightness=&-saturation=&-contrast=&-hue=&-flip=&-mirror=&-scene=] |
| parameters | brightness | Brightness 0-255 |
|  | saturation | Saturation 0-255 |
|  | contrast | Contrast 0-255 |
|  | hue | Color 0-127 |
|  | scene | White Balance: auto indoor outdoor |
|  | flip | Image flip: on off |
|  | mirror | Image mirror: on off |
| Return Value | Success: contain Success Failure: contain Error |
| Note | Different device type supports different image parameters, reference to Appendix I: Definition of device type |
| Example | /cgi-bin/hi3510/param.cgi?cmd=setimageattr&-brightness=1&-saturation=1&-contrast=1&-hue=1&-flip=on&-mirror=on&-scene=indoor& |

## param.cgi?cmd=getoverlayattr

| Function | To get OSDparameters |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=getoverlayattr&-region=] |
| parameters | region | region 0: OSD time region 1: OSD name region |
| Return Value | x_[region] | OSD region x Coordinate |
|  | y_[region] | OSD region y Coordinate |
|  | w_[region] | OSD region width |
|  | h_[region] | OSD region height |
|  | show_[region] | OSD show/hide 0: hide 1: show |
|  | name_[region] | OSD name |
| Note | None |
| Example | /cgi-bin/hi3510/param.cgi?cmd=getoverlayattr&-region=0 |

## param.cgi?cmd=setoverlayattr

| Function | To set OSD parameters |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=setoverlayattr&-region=&show=&name=] |
| parameters | region | region 0: OSD time region 1: OSD name region |
|  | show | OSD show/hide 0: hide 1: show |
|  | name | OSD name , Support English characters only. Length can not exceed 16 characters |
| Return Value | Success: contain Success Failure: contain Error |
| Note | Attention: region_0 time OSD region does not support set name parameters |
| Example | /cgi-bin/hi3510/param.cgi?cmd=setoverlayattr&-region=0&-show=0 |
|  | /cgi-bin/hi3510/param.cgi?cmd=setoverlayattr&-region=1&-show=1&-name=IPCam |

## param.cgi?cmd=getmobilesnapattr

| Function | To get mobile snapshot attributes parameters |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=getmobilesnapattr] |
| parameters | None |
| Return Value | msize | 1: sub-stream max resolution 2: sub-stream min resolution |
| Note | Some device does not support to change these attributes , reference to Appendix I: Definition of device type |
| Example | /cgi-bin/hi3510/param.cgi?cmd=getmobilesnapattr |

## param.cgi?cmd=setmobilesnapattr

| Function | To set mobile snapshot attributes parameters |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=setmobilesnapattr&-msize=] |
| parameters | msize | 1: sub-stream max resolution 2: sub-stream min resolution |
| Return Value | Success: contain Success Failure: contain Error |
| Note | Some device does not support to change these attributes , reference to Appendix I: Definition of device type |
| Example | /cgi-bin/hi3510/param.cgi?cmd=setmobilesnapattr&-msize=1 |

## param.cgi?cmd=getaencattr

| Function | To get audio codec parameters |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=getaencattr&-chn=] |
| parameters | chn | Channel number: 11: main-stream 12: sub-stream |
| Return Value | aeswitch_1 or aeswitch_2 | Audio Codec Switch 0: dissable 1: enable |
|  | aeformat_1 or aeformat_2 | Audio Codec Format g711a: G711 a-law 64Kbps g726: G726 16Kbps |
| Note | _1 is main-stream ,_2 is sub-stream . Audio Sampling rate: 8K, Mono, 16 bit |
| Example | /cgi-bin/hi3510/param.cgi?cmd=getaencattr&-chn=11 |

## param.cgi?cmd=setaencattr

| Function | To set audio codec parameters |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=setaencattr&-chn=] |
| parameters | chn | Channel number: 11: main-stream 12: sub-stream |
|  | aeswitch | Audio Codec Switch 0: dissable 1: enable |
|  | aeformat | Audio Codec Format g711a: G711 a-law 64Kbps g726: G726 16Kbps |
| Return Value | Success: contain Success Failure: contain Error |
| Note | Audio Sampling rate: 8K, Mono, 16 bit |
| Example | /cgi-bin/hi3510/param.cgi?cmd=setaencattr&-chn=11&-aeswitch=0 |
|  | /cgi-bin/hi3510/param.cgi?cmd=setaencattr&-chn=12&-aeswitch=1&-aeformat=g726 |

## param.cgi?cmd=getaudioinvolume

| Function | To get volume value |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=getaudioinvolume] |
| parameters | None |
| Return Value | volume | Range: 1-127 |
| Note | None |
| Example | /cgi-bin/hi3510/param.cgi?cmd=getaudioinvolume |

## param.cgi?cmd=setaudioinvolume

| Function | To set volume value |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=setaudioinvolume&-volume=] |
| parameters | volume | Range: 1-127 |
| Return Value | Success: contain Success Failure: contain Error |
| Note | None |
| Example | /cgi-bin/hi3510/param.cgi?cmd=setaudioinvolume&-volume=100 |

# 2 Infrared LED Control

## param.cgi?cmd=getinfrared

| Function | To get Infrared LED parameters |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=getinfrared] |
| parameters | None |
| Return Value | infraredstat | Infrared LED Status: auto open close |
| Note | Some device does not support to change these attributes , reference to Appendix I: Definition of device type |
| Example | /cgi-bin/hi3510/param.cgi?cmd=getinfrared |

## param.cgi?cmd=setinfrared

| Function | To set Infrared LED parameters |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=setinfrared] |
| parameters | None |
| Return Value | infraredstat | Infrared LED Status: auto open close |
| Note | Some device does not support to change these attributes , reference to Appendix I: Definition of device type |
| Example | /cgi-bin/hi3510/param.cgi?cmd=setinfrared&-infraredstat=auto |

# 3 Network

## param.cgi?cmd=getnetattr

| Function | To get network parameters |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=getnetattr] |
| parameters | None |
| Return Value | dhcpflag | DHCP: on: enable off: disable |
|  | ip | IP address |
|  | netmask | xxx.xxx.xxx.xxx |
|  | gateway | xxx.xxx.xxx.xxx |
|  | dnsstat | DNS status: 0: manual 1: auto |
|  | fdnsip | Primary DNS |
|  | sdnsip | The second DNS |
|  | macaddress | MAC address |
|  | networktype | Network type: LAN WiFi |
| Note | None |
| Example | /cgi-bin/hi3510/param.cgi?cmd=getnetattr |

## param.cgi?cmd=setnetattr

| Function | To config LAN parameters of device |
| --- | --- |
| Authority | Admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=setnetattr&-dhcp=&-ipaddr=&-netmask=&-gateway=&-dnsstat=&-fdnsip=&-sdnsip=] |
| parameters | dhcp | DHCP: on: enable off: disable |
|  | ipaddr | IP address |
|  | netmask | xxx.xxx.xxx.xxx |
|  | gateway | xxx.xxx.xxx.xxx |
|  | dnsstat | DNS status: 0: manual 1: auto |
|  | fdnsip | Primary DNS |
|  | sdnsip | The second DNS |
| Return Value | Success: contain Success Failure: contain Error |
| Note | None |
| Example | /cgi-bin/hi3510/param.cgi?cmd=setnetattr&-dhcp=off&-ipaddr=192.168.1.88&-netmask=255.255.255.0&-gateway=192.168.1.1&-dnsstat=0&-fdnsip=192.168.1.1&-sdnsip= |

## param.cgi?cmd=gethttpport

| Function | To get HTTP port |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=gethttpport] |
| parameters | None |
| Return Value | httpport | HTTP port |
| Note | None |
| Example | /cgi-bin/hi3510/param.cgi?cmd=gethttpport |

## param.cgi?cmd=sethttpport

| Function | To config HTTP port |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=sethttpport&-httpport=] |
| parameters | httpport | HTTP port : range [80~49151] |
| Return Value | Success: contain Success Failure: contain Error |
| Note | Device will automatically restart when the configuration is successful |
| Example | /cgi-bin/hi3510/param.cgi?cmd=sethttpport&-httpport=80 |

## param.cgi?cmd=getrtspport

| Function | To get rtsp port |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=getrtspport] |
| parameters | None |
| Return Value | rtspport | RTSP port |
| Note | None |
| Example | /cgi-bin/hi3510/param.cgi?cmd=getrtspport |

## param.cgi?cmd=setrtspport

| Function | To config RTSP port |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=setrtspport&-rtspport=] |
| parameters | Rtsp port | RTSP port range: [80~49151] |
| Return Value | Success: contain Success Failure: contain Error |
| Note | Device will automatically restart when the configuration is successful |
| Example | /cgi-bin/hi3510/param.cgi?cmd=setrtspport&-rtspport=554 |

## param.cgi?cmd=getinternetip

| Function | To inquiry the Internet IP address of this device |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=getinternetip] |
| parameters | None |
| Return Value | internetip | Web IP address ,for example: var internetip="220.112.14.173" |
| Note | None |
| Example | /cgi-bin/hi3510/param.cgi?cmd=getinternetip |

## param.cgi?cmd=getupnpattr

| Function | To get UPNP parameters |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=getupnpattr] |
| parameters | None |
| Return Value | upm_enable | UPNP port map : 0: disable 1: enable |
| Note | None |
| Example | /cgi-bin/hi3510/param.cgi?cmd=getupnpattr |

## param.cgi?cmd=setupnpattr

| Function | To set UPNP parameters |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=setupnpattr&-upm_enable=] |
| parameters | upm_enable | UPNP port map : 0: disable 1: enable |
| Return Value | Success: contain Success Failure: contain Error |
| Note | None |
| Example | /cgi-bin/hi3510/param.cgi?cmd=setupnpattr&-upm_enable=1 |

# 4 Wi-Fi setting

## param.cgi?cmd=getwirelessattr

| Function | To get wifi parameters |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=getwirelessattr] |
| parameters | None |
| Return Value | wf_enable | Wifi Switch 0: Turn off 1: Turn on |
|  | wf_ssid | SSID Max 32 english characters |
|  | wf_auth | Encryption: 0: None 1: WEP 2: WPA-PSK 3: WPA2-PSK |
|  | wf_key | Wi-Fi Key |
|  | wf_enc | Key type 0: TKIP 1: AES |
|  | wf_mode | Connection mode: 0: Route mode 1: Peer to peer mode |
| Note | None |
| Example | /cgi-bin/hi3510/param.cgi?cmd=getwirelessattr |

## param.cgi?cmd=setwirelessattr

| Function | To set Wi-Fi parameters |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=setwirelessattr&-wf_enable=&-wf_ssid=&-wf_auth=&-wf_key=&-wf_enc=&-wf_mode=] |
| parameters | wf_enable | Wifi Switch 0: Turn off 1: Turn on |
|  | wf_ssid | SSID Max 32 english characters |
|  | wf_auth | Encryption: 0: None 1: WEP 2: WPA-PSK 3: WPA2-PSK |
|  | wf_key | Wi-Fi Key |
|  | wf_enc | Key type 0: TKIP 1: AES |
|  | wf_mode | Connection mode: 0: Route mode 1: Peer to peer mode |
| Return Value | Success: contain Success Failure: contain Error |
| Note | None |
| Example | /cgi-bin/hi3510/param.cgi?cmd=setwirelessattr&-wf_ssid=linksys&-wf_enable=1&-wf_auth=2&-wf_key=1234567890&-wf_enc=0&-wf_mode=0 |

## param.cgi?cmd=searchwireless

| Function | To scan Wi-Fi network |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=searchwireless] |
| parameters | None |
| Return Value | waccess_points | Number of Access Point |
|  | wchannel | Channel |
|  | wrssi | Signal strength |
|  | wessid | SSID |
|  | wenc | Encryption |
|  | wauth | Authentication |
|  | wnet | Connection mode ( Route mode or peer to peer mode) |
|  | Attention :If there are several Access Point, (waccess_points >1), This CGI command will return field value of “wchannel “to “wnet” except access_points,for examples: var waccess_points="2" ; var wchannel=new Array(); var wrssi=new Array(); var wessid=new Array(); var wenc=new Array(); var wauth=new Array(); var wnet=new Array(); wchannel[0]="6" ; wrssi[0]="-82" ; wessid[0]="Fumax wireless" ; wenc[0]="AES" ; wauth[0]="WPA(2)-PSK" ; wnet[0]="Infra" ; wchannel[1]="11" ; wrssi[1]="-62" ; wessid[1]="linksys" ; wenc[1]="TKIP" ; wauth[1]="WPA(2)-PSK" ; wnet[1]="Infra" ; |
| Note | None |
| Example | /cgi-bin/hi3510/param.cgi?cmd=searchwireless |

## param.cgi?cmd=chkwirelessattr

| Function | To check Wi-Fi parameters |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=chkwirelessattr&-wf_ssid=&-wf_auth=&-wf_key=&-wf_enc=&-wf_mode=] |
|  | wf_ssid | SSID Max 32 english characters |
|  | wf_auth | Encryption 0: None 1: WEP 2: WPA-PSK 3: WPA2-PSK |
|  | wf_key | Wi-Fi Key |
|  | wf_enc | Key type 0: TKIP 1: AES |
|  | wf_mode | Connection mode: 0: Route mode 1: Peer to peer mode |
| Return Value | wf_result | WIFI check Return Value 0: failure 1: success |
| Note | None |
| Example | /cgi-bin/hi3510/param.cgi?cmd=chkwirelessattr&-wf_ssid=linksys&-wf_auth=2&-wf_key=1234567890&-wf_enc=0&-wf_mode=0 |

# 5 DDNS

## param.cgi?cmd=get3thddnsattr

| Function | To get DDNS parameters |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=get3thddnsattr] |
| parameters | None |
| Return Value | d3th_enable | DDNS: 0: disable 1: enable |
|  | d3th_service | DDNS Service providers : 0: dyndns.org 1: 322.org 2: dynddns.us |
|  | d3th_uname | User name |
|  | d3th_passwd | password |
|  | d3th_domain | Domain name |
| Note | None |
| Example | /cgi-bin/hi3510/param.cgi?cmd=get3thddnsattr |

## param.cgi?cmd=set3thddnsattr

| Function | To set DDNS parameters |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi?cmd=set3thddnsattr.[?-d3th_enable=&-d3th_service=&-d3th_uname=&-d3th_passwd=&-d3th_domain=] |
| parameters | d3th_enable | DDNS: 0: disable 1: enable |
|  | d3th_service | DDNS Service providers : 0: dyndns.org 1: 322.org 2: dynddns.us |
|  | d3th_uname | User name |
|  | d3th_passwd | password |
|  | d3th_domain | Domain name |
| Return Value | Success: contain Success Failure: contain Error |
| Note | None |
| Example | /cgi-bin/hi3510/param.cgi?cmd=set3thddnsattr&-d3th_enable=1&-d3th_service=1&-d3th_uname=sample&-d3th_passwd=1234&-d3th_domain=sample.dyndns.org |

# 6 PTZ

## ptzctrl.cgi

| Function | To control PTZ |
| --- | --- |
| Authority | admin and user |
| Syntax | /cgi-bin/hi3510/ptzctrl.cgi[?-step=&-act=&-speed=] |
| parameters | step | Step Mode: 0: After step run , PTZ needs new CGI command to stop 1: After step run, PTZ stop automatically |
|  | act | Control command string , for example: left right up down home zoom in zoom out hscan vscan stop |
|  | speed | PTZ speed , range 1~63 . |
| Return Value | Success: contain Success Failure: contain Error |
| Note | Different device type support different PTZ parameters, reference to Appendix I: Definition of device type |
| Example | /cgi-bin/hi3510/ptzctrl.cgi?-step=0&-act=left&-speed=45 |

## preset.cgi

| Function | To preset PTZ |
| --- | --- |
| Authority | Admin and user |
| Syntax | /cgi-bin/hi3510/preset.cgi[?-act=&-status=&-number=] |
| parameters | act | Command : goto: go to preset position set: set preset position |
|  | status | Preset command: 0: clear 1: save |
|  | number | Preset position number |
| Return Value | Success: contain Success Failure: contain Error |
| Note | Different device type support different preset number parameters, reference to Appendix I: Definition of device type |
| Example | /cgi-bin/hi3510/preset.cgi?-act=goto&-number=1 /cgi-bin/hi3510/preset.cgi?-act=set&-status=1&-number=1 |

## param.cgi?cmd=getptzcomattr

| Function | To get PTZ parameters |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=getptzcomattr] |
| parameters | None |
| Return Value | protocal | Protocol type: 0: PELCO-D 1: PELCO-P |
|  | address | Address code （0~255） |
|  | baud | Baud rate |
|  | databit | Data width |
|  | stopbit | Stop bit |
|  | check | Parity: 0: None 1: odd parity 2: even parity 3: mark 4: space |
| Note | Some device does not support this attribute , reference to Appendix I: Definition of device type |
| Example | /cgi-bin/hi3510/param.cgi?cmd=getptzcomattr |

## param.cgi?cmd=setptzcomattr

| Function | To set PTZ parameters |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=setptzcomattr&-protocal=&-address=&-baud=&-databit=&-stopbit=&-check=] |
| parameters | protocal | Protocol type: 0: PELCO-D 1: PELCO-P |
|  | address | Address code: 0~255 |
|  | baud | Baud rate: 1200、2400、4800、9600、19200、38400、 57600 |
|  | databit | Data width: 7 or 8 |
|  | stopbit | Stop bit: 1or 2 |
|  | check | Parity: 0: None 1: odd parity 2: even parity |
| Return Value | Success: contain Success Failure: contain Error |
| Note | Some device does not support this attribute , reference to Appendix I: Definition of device type |
| Example | /cgi-bin/hi3510/param.cgi?cmd=setptzcomattr&-protocal=0&-address=1&-baud=9600&-databit=8&-stopbit=1&-check=0 |

## ptzup.cgi

| Function | To control PTZ upward movement for mobile |
| --- | --- |
| Authority | admin and user |
| Syntax | /cgi-bin/hi3510/ptzup.cgi |
| parameters | None |
| Return Value | Success: contain Success Failure: contain Error |
| Note | None |
| Example | /cgi-bin/hi3510/ptzup.cgi |

## ptzdown.cgi

| Function | To control PTZ downward movement for mobile |
| --- | --- |
| Authority | admin and user |
| Syntax | /cgi-bin/hi3510/ptzdown.cgi |
| parameters | None |
| Return Value | Success: contain Success Failure: contain Error |
| Note | None |
| Example | /cgi-bin/hi3510/ptzdown.cgi |

## ptzleft.cgi

| Function | To control PTZ left movement for mobile |
| --- | --- |
| Authority | admin and user |
| Syntax | /cgi-bin/hi3510/ptzleft.cgi |
| parameters | None |
| Return Value | Success: contain Success Failure: contain Error |
| Note | None |
| Example | /cgi-bin/hi3510/ptzleft.cgi |

## ptzright.cgi

| Function | To control PTZ right movement for mobile |
| --- | --- |
| Authority | admin and user |
| Syntax | /cgi-bin/hi3510/ptzright.cgi |
| parameters | None |
| Return Value | Success: contain Success Failure: contain Error |
| Note | None |
| Example | /cgi-bin/hi3510/ptzright.cgi |

## ptzzoomin.cgi

| Function | To zoom in for mobile |
| --- | --- |
| Authority | admin and user |
| Syntax | /cgi-bin/hi3510/ptzzoomin.cgi |
| parameters | None |
| Return Value | Success: contain Success Failure: contain Error |
| Note | None |
| Example | /cgi-bin/hi3510/ ptzzoomin.cgi |

## ptzzoomout.cgi

| Function | To zoom out for mobile |
| --- | --- |
| Authority | admin and user |
| Syntax | /cgi-bin/hi3510/ptzzoomout.cgi |
| parameters | None |
| Return Value | Success: contain Success Failure: contain Error |
| Note | None |
| Example | /cgi-bin/hi3510/ptzzoomout.cgi |

# 7 Motion detection and I/O Alarm

## param.cgi?cmd=getmdattr

| Function | To get motion detection parameters |
| --- | --- |
| Authority | admin |
| Syntax | cgi-bin/hi3510/param.cgi[?cmd=getmdattr] |
| parameters | None |
| Return Value | m1_enable | The first motion detection region: 0: disable 1: enable |
|  | m1_x | Region 1 abscissa |
|  | m1_y | Region 1 Ordinate |
|  | m1_w | Region 1 width |
|  | m1_h | Region 1 height |
|  | m1_sensitivity | Region 1 sensitivity |
|  | m1_threshold | Reserved, unused |
|  | m2_enable | The second motion detection region: 0: 关闭 1: 启用 |
|  | m2_x | Region 2 abscissa |
|  | m2_y | Region 2 Ordinate |
|  | m2_w | Region 2 width |
|  | m2_h | Region 2 height |
|  | m2_sensitivity | Region 2 sensitivity |
|  | m2_threshold | Reserved, unused |
|  | m3_enable | The third motion detection region: 0: disable 1: enable |
|  | m3_x | Region 3 abscissa |
|  | m3_y | Region 3 Ordinate |
|  | m3_w | Region 3 width |
|  | m3_h | Region 3 height |
|  | m3_sensitivity | Region 3 sensitivity |
|  | m3_threshold | Reserved, unused |
|  | m4_enable | The fourth motion detection region: 0: disable 1: enable |
|  | m4_x | Region 4 abscissa |
|  | m4_y | Region 4 Ordinate |
|  | m4_w | Region 4 width |
|  | m4_h | Region 4 height |
|  | m4_sensitivity | Region 4 sensitivity |
|  | m4_threshold | Reserved, unused |
| Note | The region coordinate, width and height are based the max resolution of this device. |
| Example | /cgi-bin/hi3510/param.cgi?cmd=getmdattr |

## param.cgi?cmd=setmdattr

| Function | To set motion detection parameters |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=setmdattr&-enable=&-s=&-name=&-x=&-y=&-w=&-h=] |
| parameters | enable | motion detection function: 0: disable 1: enable |
|  | s | sensitivity: range [0 ~ 100] |
|  | name | Alarm region : range[1 ~ 4] |
|  | x | motion detection region abscissa |
|  | y | motion detection region Ordinate |
|  | w | motion detection region width |
|  | h | motion detection region height |
| Return Value | Success: contain Success Failure: contain Error |
| Note | The region coordinate, width and height are based the max resolution of this device. |
| Example | /cgi-bin/hi3510/param.cgi?cmd=setmdattr&-enable=1&-s=50&-name=1&-x=0&-y=0&-w=60&-h=60 |

## param.cgi?cmd=getioattr

| Function | To get alarm IO parameters |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=getioattr] |
| parameters | None |
| Return Value | io_enable | Alarm IO: 0: disable 1: enable |
|  | io_flag | Alarm IO mode: 0: NC 1: NO |
| Note | None |
| Example | /cgi-bin/hi3510/param.cgi?cmd=getioattr |

## param.cgi?cmd=setioattr

| Function | To set alarm IO parameters |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=setioattr &-io_enable=&-io_flag=] |
| parameters | io_enable | Alarm IO: 0: disable 1: enable |
|  | io_flag | Alarm IO mode: 0: NC 1: NO |
| Return Value | Success: contain Success Failure: contain Error |
| Note | None |
| Example | /cgi-bin/hi3510/param.cgi?cmd=setioattr&-io_enable=0&-io_flag=1 |

## param.cgi?cmd=getmdalarm

| Function | To get alarm linkage parameters |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=getmdalarm&-aname=] |
| parameters | aname | option: email: E-mail alarm emailsnap: E-mail alarm and send snapshot snap: save snapshot to SD card record: save video to SD card ftprec: upload video to FTP server relay: relay output |
| Return Value | md_email_switch | E-mail alarm function: on: enable off: disable |
|  | md_emailsnap_switch | E-mail alarm and send image function: on: enable off: disable |
|  | md_snap_switch | Save snapshot to SD card: on: enable off: disable |
|  | md_record_switch | save video to SD card: on: enable off: disable |
|  | md_ftprec_switch | Upload video to FTP server: on: enable off: disable |
|  | md_relay_switch | Relay output: on: enable off: disable |
| Note | None |
| Example | /cgi-bin/hi3510/param.cgi?cmd=getmdalarm&-aname=email&cmd=getmdalarm&-aname=emailsnap&cmd=getmdalarm&-aname=snap&cmd=getmdalarm &cmd=getmdalarm&-aname=record&cmd=getmdalarm&-aname=ftprec&cmd=getmdalarm&-aname=relay |

## param.cgi?cmd=setmdalarm

| Function | To set alarm linkage parameters |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=setmdalarm &-aname=&-switch=] |
| parameters | aname | Alarm linkage option: email: E-mail alarm emailsnap: E-mail alarm and send snapshot snap: save snapshot to SD card record: save video to SD card ftprec: upload video to FTP server relay: relay output |
|  | switch | alarm linkage value: on: enable off: disable |
| Return Value | Success: contain Success Failure: contain Error |
| Note | Attention:Before upload video to FTP serve,you must enable save video to SD card. Please be sure to insert SD card,enable save snapshot and save video, in order to upload video to FTP server . |
| Example | /cgi-bin/hi3510/param.cgi?cmd=setmdalarm&-aname=email&-switch=off&cmd=setmdalarm&-aname=emailsnap&-switch=off&cmd=setmdalarm&-aname=ftprec&-switch=off&cmd=setmdalarm&-aname=snap&-switch=off&cmd=setmdalarm&-aname=record&-switch=off&cmd=setmdalarm&-aname=relay&-switch=off |

## param.cgi?cmd=getrelayattr

| Function | To get alarm linkage relay output time |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=getrelayattr] |
| parameters | None |
| Return Value | time | Output time（s） , for examplevar time="10"; |
| Note | None |
| Example | /cgi-bin/hi3510/param.cgi?cmd=getrelayattr |

## param.cgi?cmd=setrelayattr

| Function | To set alarm linkage relay output time |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=setrelayattr&-time=] |
| parameters | time | Output time（s）, range [5、10、20、30] |
| Return Value | Success: contain Success Failure: contain Error |
| Note | None |
| Example | /cgi-bin/hi3510/param.cgi?cmd=setrelayattr&-time=10 |

## param.cgi?cmd=getschedule

| Function | To get alarm and arming schedule table |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=getschedule&-type=&-ename=] |
| parameters | type | Arming type: event |
|  | ename | Alarm type: md: motion dection |
| Return Value | etm | Arming time mode: 0: All week mode 1: working days rest days mode 2: All time mode |
|  | workday | Arming time period of working days,using in working days rest days mode. |
|  | weekend | Arming time period of rest days,using in working days rest days mode. |
|  | week | Every day arming time period in All week mode |
|  | md_interval | Arm time interval |
|  | Attention: There are more groups of alarm schedule table in return value. For example: var etm="0"; var workday = "0~95," ; var weekend="0~95," ; var week= new Array() ; week[0] = "0~95,"; week[1] = "0~95,"; week[2] = "0~95,"; week[3] = "0~95,"; week[4] = "0~95,"; week[5] = "0~95,"; week[6] = "0~95,"; var md_interval="0"; |
| Note | None |
| Example | /cgi-bin/hi3510/param.cgi?cmd=getschedule&-type=event&-ename=md |

## param.cgi?cmd=setschedule

| Function | To set alarm and arming schedule table |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=setschedule&-type=&-ename=&-etm=&-workday=&-weekend=&-week0=&-week1=&-week2=&-week3=&-week4=&-week5=&-week6=] |
| parameters | type | Arming type: event |
|  | ename | Alarm type: md: motion dection |
|  | etm | Arming time mode: 0: All week mode 1: working days rest days mode 2: All time mode |
|  | workday | Arming time period of working days Format : start time~end time |
|  | weekend | Arming time period of rest days Format : start time~end time |
|  | week0 | Arming time period on Monday Format : start time~end time |
|  | week1 | Arming time period on Tuesday Format : start time~end time |
|  | week2 | Arming time period on Wednesday Format : start time~end time . |
|  | week3 | Arming time period on Thursday Format : start time~end time |
|  | week4 | Arming time period on Friday Format : start time~end time |
|  | week5 | Arming time period on Saturday Format : start time~end time |
|  | week6 | Arming time period on Sunday Format : start time~end time |
|  | Attention: workday and weekend field only used in working days rest days mode, week0 ~ week6 field only used in all week mode,and start time must be less then end time . The calculation method of these start and end time field are: If time is 0 hour 0 miniute, it will be set to “none”, Other cases according to the following formula: strart-time = start-hour * 4 + start-minute number end-time = end-hour * 4 + end-minute number - 1； One minute is split to four time period: 0(number is 0), 15(number is 1), 30(number is 2) and 45(number is 3). For example: If specify a start time of 8:30, then start-time = 8*4+2=34, If specify a end time of 8:30, then end-time = =8*4+2-1=33 |
| Note |  |
| Example | /cgi-bin/hi3510/param.cgi?cmd=setschedule&-type=event&-ename=md&-etm=1&-workday=0~33&-weekend=none /cgi-bin/hi3510/param.cgi?cmd=setschedule&-type=event&-ename=md&-etm=2 |

## param.cgi?cmd=getalarmserverattr

| Function | To get alarm server parameters |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=getalarmserverattr] |
| parameters | None |
| Return Value | as_server | Server address |
|  | as_port | Server port (1-65535) |
|  | as_username | username |
|  | as_password | password |
| Note | None |
| Example | /cgi-bin/hi3510/param.cgi?cmd=getalarmserverattr |

# 8 User Management

## param.cgi?cmd=getuserattr

| Function | To get all user information |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=getuserattr] |
| parameters | None |
| Return Value | at_name | User name |
|  | at_password | password |
| Note | This CGI command will return all user infomation , for example: var at_name0="admin"; var at_password0="admin"; var at_name1="user"; var at_password1="user"; var at_name2="guest"; var at_password2="guest"; |
| Example | /cgi-bin/hi3510/param.cgi?cmd=getuserattr |

## param.cgi?cmd=setuserattr

| Function | To set user management parameters |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=setuserattr&-at_username=&-at_password =] |
| parameters | at_username | username parameters,must be admin,user,guest |
|  | at_password | password parameters,max length must be less then 16 |
| Return Value | Success: contain Success Failure: contain Error |
| Note | None |
| Example | /cgi-bin/hi3510/param.cgi?cmd=setuserattr&-at_username=admin&-at_password=admin |

## getsetupflag.cgi

| Function | To get admin parameters |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/getsetupflag.cgi |
| parameters | None |
| Return Value | name0 | name |
|  | password0 | password |
|  | authLevel0 | reversed |
| Note | None |
| Example | /cgi-bin/hi3510/getsetupflag.cgi |

## getstreamflag.cgi

| Function | To get guest parameters |
| --- | --- |
| Authority | guest |
| Syntax | /cgi-bin/hi3510/getstreamflag.cgi |
| parameters | None |
| Return Value | name2 | name |
|  | password2 | password |
|  | authLevel2 | reversed |
| Note | None |
| Example | /cgi-bin/hi3510/getstreamflag.cgi |

## getptzflag.cgi

| Function | To get user parameters |
| --- | --- |
| Authority | user |
| Syntax | /cgi-bin/hi3510/getptzflag.cgi |
| parameters | None |
| Return Value | name1 | name |
|  | password1 | password |
|  | authLevel1 | reversed |
| Note | None |
| Example | /cgi-bin/hi3510/getptzflag.cgi |

# 9 Time Snapshot

## param.cgi?cmd=getsnaptimerattr

| Function | To get time snapshot parameters |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=getsnaptimerattr] |
| parameters | None |
| Return Value | as_enable | Time Snapshot : 0: disable 1: enable |
|  | as_interval | Time interval , minute（range: 1~1440） |
|  | as_type | Linkage type 1: save snapshot to SD card . 4: send E-mail 5: save snapshot to SD card and send E-mail. |
| Note | None |
| Example | /cgi-bin/hi3510/param.cgi?cmd=getsnaptimerattr |

## param.cgi?cmd=setsnaptimerattr

| Function | To set time snapshot parameters |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=setsnaptimerattr&-as_enable=&-as_interval=&-as_type=] |
| parameters | as_enable | Time Snapshot : 0: disable 1: enable |
|  | as_interval | Time interval , minute（range: 1~1440） |
|  | as_type | Linkage type 1: save snapshot to SD card . 4: send E-mail 5: save snapshot to SD card and send E-mail. |
| Return Value | Success: contain Success Failure: contain Error |
| Note | 3 parameters must be used together |
| Example | /cgi-bin/hi3510/param.cgi?cmd=setsnaptimerattr&-as_enable=1&-as_interval=60&-as_type=5 |

# 10 FTP

## param.cgi?cmd=getftpattr

| Function | To get FTP parameters |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=getftpattr] |
| parameters | None |
| Return Value | ft_server | FTP server address |
|  | ft_port | Server port |
|  | ft_username | username |
|  | ft_password | password |
|  | ft_mode | Passive mode: 0: disable 1: enable |
|  | ft_dirname | Path |
| Note | None |
| Example | /cgi-bin/hi3510/param.cgi?cmd=getftpattr |

## param.cgi?cmd=setftpattr

| Function | To set FTP parameters |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=getftpattr&-ft_server=&-ft_port=&-ft_username=&-ft_password=&-ft_mode=] |
| parameters | ft_server | FTP server address |
|  | ft_port | Server port |
|  | ft_username | username |
|  | ft_password | password |
|  | ft_mode | Passive mode: 0: disable 1: enable |
|  | ft_dirname | Path ,path is “./” |
| Return Value | Success: contain Success Failure: contain Error |
| Note | None |
| Example | /cgi-bin/hi3510/param.cgi?cmd=setftpattr&-ft_server=220.112.14.173&-ft_port=21&-ft_username=FTPUsername&-ft_password=FTPPassword&-ft_mode=1&-ft_dirname=abc |

# 11 SMTP

## param.cgi?cmd=getsmtpattr

| Function | To get SMTP parameters |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=getsmtpattr] |
| parameters | None |
| Return Value | ma_server | SMTP server address |
|  | ma_port | Server port |
|  | ma_ssl | Use SSL: 0: disable 1: enable |
|  | ma_logintype | authentication: 1: enable 3: disable |
|  | ma_username | username |
|  | ma_password | password |
|  | ma_from | Sender address |
|  | ma_to | Delivery Address |
|  | ma_subject | Mail subject |
|  | ma_text | Mail text |
| Note | None |
| Example | /cgi-bin/hi3510/param.cgi?cmd=getsmtpattr |

## param.cgi?cmd=setsmtpattr

| Function | To set SMTP parameters |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=setsmtpattr&-ma_server=&-ma_port=&-ma_ssl=&-ma_logintype=&-ma_username=&-ma_password=&-ma_from=&-ma_to=&-ma_subject=&-ma_text=] |
| parameters | ma_server | SMTP server address |
|  | ma_port | Server port |
|  | ma_ssl | Use SSL: 0: disable 1: enable |
|  | ma_logintype | authentication: 1: enable 3: disable |
|  | ma_username | username |
|  | ma_password | password |
|  | ma_from | Sender address |
|  | ma_to | Delivery Address |
|  | ma_subject | Mail subject |
|  | ma_text | Mail text |
| Return Value | Success: contain Success Failure: contain Error |
| Note | None |
| Example | /cgi-bin/hi3510/param.cgi?cmd=setsmtpattr&-ma_server=stmp.sdf.com&-ma_from=sd1@sdf.com&-ma_to=a1@sdf.com&-ma_subject=demosubject&-ma_text=demotext&-ma_logintype=1&-ma_username=demo&-ma_password=123456&-ma_port=25&-ma_ssl=0 |

# 12 SD Card manipulation

## sdfrmt.cgi

| Function | To format SD card to FAT32file system |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/sdfrmt.cgi |
| parameters | None |
| Return Value | Format SD Card Success |
| Note | Please wait for a long time |
| Example | /cgi-bin/hi3510/sdfrmt.cgi |

## sdstop.cgi

| Function | To stop use SD card |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/sdstop.cgi |
| parameters | None |
| Return Value | Stop SD Card Success |
| Note | Please wait for a long time |
| Example | /cgi-bin/hi3510/sdstop.cgi |

# 13 System parameter settings

## param.cgi?cmd=getserverinfo

| Function | To get device system information |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=getserverinfo] |
| parameters | None |
| Return Value | model | Device serial number |
|  | hardVersion | H/W version |
|  | softVersion | S/W version |
|  | name | Device name |
|  | startdate | System start time |
|  | runtimes | Reversed |
|  | sdstatus | SD card status out: NoneSD Ready: ready to use Readonly: SD card only support to read |
|  | sdfreespace | SD card free space (KB) |
|  | sdtotalspace | SD card total capacity(KB) |
| Note | None |
| Example | /cgi-bin/hi3510/param.cgi?cmd=getserverinfo |

## param.cgi?cmd=getdevtype

| Function | To get device type information |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=getdevtype] |
| parameters | None |
| Return Value | devtype |  |
| Note | reference to Appendix I: Definition of device type |
| Example | /cgi-bin/hi3510/param.cgi?cmd=getdevtype |

## param.cgi?cmd=getstreamnum

| Function | To get online user number |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=getstreamnum] |
| parameters | None |
| Return Value | user_num | online user number , for example: var stream_num = "1" ; |
| Note | None |
| Example | /cgi-bin/hi3510/param.cgi?cmd=getstreamnum |

## param.cgi?cmd=getservertime

| Function | To get system time |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=getservertime] |
| parameters | None |
| Return Value | time | Current date and time [yyyy][mm][dd][hh][mm][ss] time="20110802182638"; |
|  | timeZone | Time zone , timeZone="Asia/Hong_Kong"; |
|  | dstmode | Daylight saving adjust on: enable off: disable |
| Note | None |
| Example | /cgi-bin/hi3510/param.cgi?cmd=getservertime |

## param.cgi?cmd=setservertime

| Function | To set system time |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=setservertime&-time=&-timezone=&-dstmode=] |
| parameters | stime | Current date and time [yyyy].[mm].[dd].[hh].[mm].[ss] 2011.08.23.10.35.08 |
|  | timezone | Time zone: timeZone="Asia/Hong_Kong"； Attention: Please reference to Appendix II Time zone about time zone |
|  | dstmode | Daylight saving adjust on: enable off: disable |
| Return Value | Success: contain Success Failure: contain Error |
| Note | Not all time zone can adjust time automaticly in daylight saving time |
| Example | /cgi-bin/hi3510/param.cgi?cmd=setservertime&-time=2011.08.23.10.35.08&-timezone=Asia%2FHong_Kong&-dstmode=off |

## param.cgi?cmd=getntpattr

| Function | To get NTP parameters |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=getntpattr] |
| parameters | None |
| Return Value | ntpenable | NTP: 1: enable 0: disable |
|  | ntpserver | NTP server: time.nist.gov time.kriss.re.kr time.windows.com time.nuri.net |
|  | ntpinterval | Synchronized interval |
| Note | None |
| Example | /cgi-bin/hi3510/param.cgi?cmd=getntpattr |

## param.cgi?cmd=setntpattr

| Function | To set NTP parameters |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/param.cgi[?cmd=setntpattr&-ntpenable=&-ntpserver=&-ntpinterval=] |
|  | ntpenable | NTP: 1: enable 0: disable |
| parameters | ntpserver | NTP server: time.nist.gov time.kriss.re.kr time.windows.com time.nuri.net |
|  | ntpinterval | Synchronized interval: range[1 ~ 24 hour] |
| Return Value | Success: contain Success Failure: contain Error |
| Note | None |
| Example | cgi-bin/hi3510/param.cgi?cmd=setntpattr&-ntpenable=1&-ntpinterval=2&-ntpserver=time.nuri.net |

## sysreset.cgi

| Function | To restore factory default |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/sysreset.cgi |
| parameters | None |
| Return Value | None |
| Note | None |
| Example | /cgi-bin/hi3510/sysreset.cgi |

## sysreboot.cgi

| Function | To restart system |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/sysreboot.cgi |
| parameters | None |
| Return Value | None |
| Note | None |
| Example | /cgi-bin/hi3510/sysreboot.cgi |

## backup.cgi

| Function | To backup configuration data |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/backup.cgi |
| parameters | None |
| Return Value | None |
| Note | None |
| Example | /cgi-bin/hi3510/backup.cgi |

## restore.cgi

| Function | To restore configuration data |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/restore.cgi[?-setting_file=] |
| parameters | setting_file | System config file |
| Return Value | None |
| Note | This CGI only support post method , send backup config file to ipcamera. |
| Example | <form name="form6" method="post" enctype="multipart/form-data" action="cgi-bin/hi3510/restore.cgi" > <input type="file" name="setting_file" > <input type="submit" value="restore" > </form> |

## upgrade.cgi

| Function | To upgrade system firmware（Caution: it may damage system） |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/upgrade.cgi[?-filename=] |
| parameters | filename | Upgrade file name |
| Return Value | None |
| Note | This CGI only support post method , send new firmware to ipcamera. |
| Example | <form name="form5" method="post" target="retframe" enctype="multipart/form-data" action="cgi-bin/hi3510/upgrade.cgi" > <input type="file" name="setting_file" > <input type="submit" value="upgrade" > </form> |

# 14 LOG

## logsync.cgi

| Function | To get log information |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/logsync.cgi |
| parameters | None |
| Return Value | None |
| Note | Thise CGI refresh the log , visit /log/accesslog.txt to view log file text Attention:Restart will clear all log file text. |
| Example | /cgi-bin/hi3510/logsync.cgi /log/accesslog.txt |

## cleanlog.cgi

| Function | To clear log |
| --- | --- |
| Authority | admin |
| Syntax | /cgi-bin/hi3510/cleanlog.cgi[?-name=] |
| parameters | name | Clear log command : access: log name |
| Return Value | None |
| Note | Use this CGI command to clear log ,when it has too much content |
| Example | /cgi-bin/hi3510/cleanlog.cgi?-name=access |

# 15 Appendix

- Appendix I  Definition of device type

Used to identify the device type,  different device has different function .

ACSII , 32 bytes.

2bytes every one field.  The first byte is the tota- type of the field, the second byte is the sub-type of the field

| field3 | field4 |
| --- | --- |
| LEN | P |
| ‘S’ | ‘Z’ |

3). Len field  ‘S’

For example:

| ‘0’ | CMOS VGA | Brightness, contrast, saturation, color, indoor, outdoor, IR LED switch, flip, mirror. main-stream :VGA, QVGA, QQVGA sub-stream : QVGA, QQVGA |
| --- | --- | --- |
| ‘2’ | CCD D1 | Brightness, contrast, saturation, color main-stream : D1,CIF,QCIF sub-stream : CIF,QCIF |
| ‘7’ | CMOS 720P | Brightness, contrast (1-7), saturation, flip, mirror main-stream : 720P, Q720P, QQ720P sub-stream : Q720P, QQ720P mobile image size does not support change |

4). PTZ field ‘Z’

For example:

| ‘0’ | Custom PTZ | up , down , left , right , vscan , hscan , home , preset（max 8 position） does not support setting by serial port , does not support PTZ speed |
| --- | --- | --- |
| ‘3’ | 485PTZ | Up, down, left, right, zoom in, zoom out, go presetposition can set 485 Property |

## Appendix II  Time zone

| Time zone field | Description |
| --- | --- |
| Etc/GMT-12 | (GMT-12:00) date line west |
| Pacific/Apia | (GMT-11:00) Midway, Samoan Islands |
| Pacific/Honolulu | (GMT-10:00) Hawaii |
| America/Anchorage | (GMT-09:00) Alaska |
| America/Los_Angeles | (GMT-08:00) Pacific Time（US and Canada） |
| America/Denver | (GMT-07:00) Mountain Time（US and Canada） |
| America/Tegucigalpa | (GMT-07:00) Chihuahua,La Paz, Mazatlan |
| America/Phoenix | (GMT-07:00) Arizona |
| America/Winnipeg | (GMT-06:00) Saskatchewan |
| America/Mexico_City | (GMT-06:00) Guadalajara, Mexico City, Monterrey |
| America/Chicago | (GMT-06:00) Central Time （US and Canada） |
| America/Costa_Rica | (GMT-06:00) Central America |
| America/Indianapolis | (GMT-05:00) Indiana (East) |
| America/New_York | (GMT-05: 00) Eastern Time (U.S. and Canada) |
| America/Bogota | (GMT-05: 00) Bogota, Lima, Rio Branco |
| America/Santiago | (GMT-04: 00) Santiago |
| America/Caracas | (GMT-04: 00) La Paz |
| America/Montreal | (GMT-04: 00) Atlantic Time (Canada) |
| America/St_Johns | (GMT-03: 30) Newfoundland |
| America/Thule | (GMT-03: 00) Greenland |
| America/Buenos_Aires | (GMT-03: 00) Buenos Aires, Georgetown |
| America/Sao_Paulo | (GMT-03: 00) Brasilia |
| Atlantic/South_Georgia | (GMT-02: 00) Mid-Atlantic |
| Atlantic/Cape_Verde | (GMT-01: 00) Cape Verde Islands |
| Atlantic/Azores | (GMT-01: 00) Azores |
| Europe/Dublin | (GMT) Greenwich Mean Time: Dublin, Edinburgh, London, Lisbon |
| Africa/Casablanca | (GMT) Casablanca, Monrovia, Reykjavik |
| Europe/Amsterdam | (GMT +01:00) Amsterdam, Berlin, Bern, Rome, Stockholm, Vienna |
| Europe/Belgrade | (GMT +01:00) Belgrade, Bratislava, Budapest, Ljubljana, Prague |
| Europe/Brussels | (GMT +01:00) Brussels, Copenhagen, Madrid, Paris |
| Europe/Warsaw | (GMT +01:00) Sarajevo, Skopje, Warsaw, Zagreb |
| Africa/Lagos | (GMT +01:00) West Central |
| Europe/Athens | (GMT +02:00) Athens, Istanbul, Minsk |
| Europe/Bucharest | (GMT +02:00) Bucharest |
| Africa/Cairo | (GMT +02:00) Cairo |
| Africa/Harare | (GMT +02:00) Harare, Pretoria |
| Europe/Helsinki | (GMT +02:00) Helsinki, Kiev, Riga, Sofia, Tallinn, Vilnius |
| Asia/Jerusalem | (GMT +02:00) Jerusalem |
| Asia/Baghdad | (GMT +03:00) Baghdad |
| Asia/Kuwait | (GMT +03:00) Kuwait, Riyadh |
| Europe/Moscow | (GMT +03:00) Moscow, St. Petersburg, Volgograd |
| Africa/Nairobi | (GMT +03:00) Nairobi |
| Asia/Tehran | (GMT +03:30) Tehran |
| Asia/Dubai | (GMT +04:00) Abu Dhabi, Muscat |
| Asia/Baku | (GMT +04:00) Baku, Tbilisi, Yerevan |
| Asia/Kabul | (GMT +04:30) Kabul |
| Asia/Yekaterinburg | (GMT +05:00) Ekaterinburg |
| Asia/Karachi | (GMT +05:00) Islamabad, Karachi, Tashkent |
| Asia/Calcutta | (GMT +05:30) Madras, Calcutta, Mumbai, New Delhi |
| Asia/Katmandu | (GMT +05:45) Kathmandu |
| Asia/Almaty | (GMT +06:00) Almaty, Novosibirsk |
| Asia/Dhaka | (GMT +06:00) Astana, Dhaka |
| Asia/Colombo | (GMT +06:00) Colombo |
| Asia/Rangoon | (GMT +06:30) Rangoon |
| Asia/Bangkok | (GMT +07:00) Bangkok, Hanoi, Jakarta |
| Asia/Krasnoyarsk | (GMT +07:00) Krasnoyarsk |
| Asia/Hong_Kong | (GMT +08:00) Beijing, Chongqing, Hong Kong, Urumqi |
| Asia/Irkutsk | (GMT +08:00) Irkutsk, Ulaanbaatar map |
| Asia/Kuala_Lumpur | (GMT +08:00) Kuala Lumpur, Singapore |
| Australia/Perth | (GMT +08:00) Perth |
| Asia/Taipei | (GMT +08:00) Taipei |
| Asia/Tokyo | (GMT +09:00) Osaka, Sapporo, Tokyo |
| Asia/Seoul | (GMT +09:00) Seoul |
| Asia/Yakutsk | (GMT +09:00) Yakutsk |
| Australia/Adelaide | (GMT +09:30) Adelaide |
| Australia/Brisbane | (GMT +10:00) Brisbane |
| Australia/Sydney | (GMT +10:00) Canberra, Melbourne, Sydney |
| Pacific/Guam | (GMT +10:00) Guam, Port Moresby |
| Australia/Hobart | (GMT +10:00) Hobart |
| Asia/Vladivostok | (GMT +10:00) Vladivostok |
| Asia/Magadan | (GMT +11:00) Majia Disi Qin, Solomon Islands, New Caledonia |
| Pacific/Auckland | (GMT +12:00) Auckland, Wellington |
| Pacific/Fiji | (GMT +12:00) Fiji, Kamchatka, Marshall Islands |
| Pacific/Tongatapu | (GMT +13:00) Nuku'alofa |